UDI NIC Test Specification

by

Gian-Carlo Bava (SCO)

Barry Feild (SCO)

Change History

| Revision | Date | Description |
| --- | --- | --- |
| 0.6 | 11/05/99 | DRAFT version for review |

Approvers:

TBD

# Introduction

This document describes the UDI Network Interface Controller (NIC) driver tests. UDI NIC driver tests verify UDI network driver channel operations, parameters, and sequences. Both send and receive are tested, as well as multiple NICs and stress.

This document defines test purposes for the UDI NIC driver test suite. Test purposes specify an operation for the driver to perform and an expected result for the operation. It also defines test cases which are a series of functional tests comprised of one or more test purposes.

## References

This document references and depends upon the following documents

UDI NIC Driver Specification, Revision 1.0

# Network Driver Test Purpose Definitions

Test purposes are the smallest addressable component used by a test case. Each test purpose specifies an operation for the driver to perform and an expected result for the operation. The test purpose generates a PASS or FAIL result based on the comparison of the actual result of the operation with the expected result. The test specification defines the operations for the driver to perform and the expected results of those operations. It does not describe how to implement the test operations.

Network drivers must implement all of the channel operations defined in the UDI NIC Driver Specification. The table below defines the NIC driver test purposes.

Most values in the Input Parameters/Notes column define parameters passed to the test purpose. These modify the test purpose behavior. Notes are in Italics and values that are variable are enclosed in <>.

Values in the Expected Results column are parameters passed by the operation, or members in a control block passed by the operation. Refer to the UDI NIC Driver Specification to differentiate parameters from structure members.

| Purpose | Chan | Orig | Operation | Input Parameters/Notes | Expected Results |
| --- | --- | --- | --- | --- | --- |
| bind | ctrl | NSR | udi_nd_bind_req |  |  |
|  | ctrl | ND | udi_nsr_bind_ack |  | status=ok/invalid_state |
| unbind | ctrl | NSR | udi_nd_unbind_req |  |  |
|  | ctrl | ND | udi_nsr_unbind_ack |  | status=ok/invalid_state |
| enable | ctrl | NSR | udi_nd_enable_req |  |  |
|  | ctrl | ND | udi_nd_enable_ack |  | status=ok/hw_problem |
| disable | ctrl | NSR | udi_nd_disable_req |  |  |
| addmulti | ctrl | NSR | udi_nd_ctrl_req, command = 1 | indicator=<add_num > data=<mac_addresses> |  |
|  | ctrl | ND | udi_nsr_ctrl_ack |  | status=ok/not_understood |
| delmulti | ctrl | NSR | udi_nd_ctrl_req, command = 2 | indicator=<del_num> data=<mac_addresses> |  |
|  | ctrl | ND | udi_nsr_ctrl_ack |  | status=ok/not_understood |
| allmultion | ctrl | NSR | udi_nd_ctrl_req, command = 3 |  |  |
|  | ctrl | ND | udi_nsr_ctrl_ack |  | status=ok/not_understood |
| allmultioff | ctrl | NSR | udi_nd_ctrl_req, command = 4 | indicator=<add_num> data=<mac_addresses> |  |
|  | ctrl | ND | udi_nsr_ctrl_ack |  | status=ok/not_understood |
| getcurrmac | ctrl | NSR | udi_nd_ctrl_req, command = 5 |  |  |
|  | ctrl | ND | udi_nsr_ctrl_ack |  | status=ok/not_understood |
| setcurrmac | ctrl | NSR | udi_nd_ctrl_req, command = 6 | indicator=<addr_size> data=<mac_address> |  |
|  | ctrl | ND | udi_nsr_ctrl_ack |  | status=ok/not_understood |
| getfactmac | ctrl | NSR | udi_nd_ctrl_req, command = 7 |  |  |
|  | ctrl | ND | udi_nsr_ctrl_ack |  | status=ok/not_understood indicator=<addr_size> data=<mac_address> |
| promiscon | ctrl | NSR | udi_nd_ctrl_req, command = 8 |  |  |
|  | ctrl | ND | udi_nsr_ctrl_ack |  | status=ok/not_understood |
| promiscoff | ctrl | NSR | udi_nd_ctrl_req, command = 9 |  |  |
|  | ctrl | ND | udi_nsr_ctrl_ack |  | status=ok/not_understood |
| hwreset | ctrl | NSR | udi_nd_ctrl_req, command = 10 |  |  |
|  | ctrl | ND | udi_nsr_ctrl_ack |  | status=ok/not_understood |
| badrxpkt | ctrl | NSR | udi_nd_ctrl_req, command = 11 | indicator=<frame_size> |  |
|  | ctrl | ND | udi_nsr_ctrl_ack |  | status=ok/not_understood |
| status | ctrl | ND | udi_nsr_status_ind | manually [un]plug NIC link state initiates ind | event=down/up/reset |
| info | ctrl | NSR | udi_nd_info_req | reset_stats=true/false timeout=<seconds> -1 for no timeout |  |
|  | ctrl | ND | udi_nsr_info_ack |  | interface_is_active=true/false OR timeout triggered |
| tx | tx | ND | udi_nsr_tx_rdy | tx_buf must be NULL |  |
|  | tx | NSR | udi_nd_tx_req | chain=<num_frames> data=<packet_headers> size=<frame_size> urgent=true/false |  |
| tx-exp | tx | ND | udi_nsr_tx_rdy |  |  |
|  | tx | NSR | udi_nd_exp_tx_req | chain=<num_frames> data=<packet_headers> size=<frame_size> urgent=true/false |  |
| rx | rx | NSR | udi_nd_rx_rdy | chain=<num_frames> data=<packet_headers> size=<frame_size> timeout=<seconds> -1 for no timeout |  |
|  | rx | ND | udi_nd_rx_ind |  | timeout triggered OR rx_status=0 actual_frame_size=size actual_frame_header=data frame_data=<testpattern> |
| rx-exp | rx | NSR | udi_nd_rx_rdy | chain=<num_frames> data=<packet_headers>size=<expected_size> timeout=<seconds> -1 for no timeout |  |
|  | rx | ND | udi_nsr_exp_rx_ind | TBD – can we test this? | timeout triggered OR rx_status=0 actual_frame_size=size actual_frame_header=data frame_data=<testpattern> |

# NIC Driver Test Case Definitions

Test cases are a series of functional tests. Functional tests are formed by combining one or more test purposes to test specific functionality. Each functional test generates a PASS or FAIL result. If one or more of the test purposes returns a FAIL result, the functional test returns a FAIL result. If one or more functional tests within a test case returns a FAIL result, the test case returns a FAIL result.

NOTE: Some of the functional tests require at least two machines to interact. These functional tests require the machines to use some type of synchronization and message exchange protocol. Such a protocol is not defined in this document. Driver configuration, initialization, and synchronization need to be described in the UDI NIC Test Case Design document.

## NIC Driver Unit Test Case

The NIC driver unit test case performs functional testing of all channel operations defined in the UDI NIC Driver Specification. This test case verifies basic functionality of the driver under test. This test case also exercises all of the valid state transitions defined in the UDI NIC Driver Specification to verify driver compliance.

This test does not verify driver behavior under heavy load or stress, nor does it attempt to verify driver behavior when presented with invalid state transitions. This test case does not attempt operations with invalid parameters.

In the Functional Test column, state transitions are delineated with arrows (->) between two states. Operations attempted in a given state are marked <state>, <operation>.

Expected results refer to the final test purpose result in the Expected Results column.

NOTE: Two state transitions (enabled->active and active->enabled) occur when the driver detects link activation or loss, respectively. It may be desirable to break this test case into two separate test cases, one that is run with the adapter plugged into the media and another that is run with the adapter unplugged. This would reduce the need for manual intervention, making the test suite as a whole more automated.

| Functional Test | Test Purpose Sequence | Input Parameters/Notes | Expected Results |
| --- | --- | --- | --- |
| unbound->bound | bind |  | status=ok |
| bound->unbound | bind, unbind |  | status=ok |
| bound->enabled | bind, enable | adapter unplugged | status=ok |
| enabled->bound | bind, enable, disable | adapter unplugged |  |
| enabled->unbound | bind, enable, unbind | adapter unplugged | status=ok |
| enabled->active | bind, enable, *plugin NIC*, status | requires manual intervention | event=up |
| active->enabled | bind, enable, *unplug NIC*, status | requires manual intervention | event=down |
| active->unbound | bind, enable, unbind |  | status=ok |
| active, transmit | bind, enable, tx | chain=1 size=<min to max pdu> data=<valid_header> urgent=false | receiver verifies frame header matches expected header (data) and frame contents are test pattern and generates pass/fail |
| active, tx-cb_ret | bind, enable, tx | chain=1 size=<min to max pdu> data=<valid_header> urgent=true NSR verifies tx cbs returned | receiver verifies frame header matches expected header (data) and frame contents are test pattern and generates pass/fail |
| active, tx-chain | bind, enable, tx | chain=<num_tx_cbs> size=<min to max pdu data=<valid_header> urgent=false | receiver verifies frame header matches expected header (data) and frame contents are test pattern and generates pass/fail |
| active, tx-exp | bind, enable, tx-exp | chain=1 size=<min to max pdu> data=<valid_header> urgent=false | receiver verifies frame header matches expected header (data) and frame contents are test pattern and generates pass/fail |
| active, rx | bind, enable, rx | timeout=<tbd> chain=1 size=<min to max pdu> data=<both unicast and broadcast MAC addr hdr> | rx_status=0 actual_frame_size=size actual_frame_header=data frame_data=<testpattern> |
| active, addmulti | bind, enable, addmulti, rx (rx to verify receive on each valid multicast addresses) | indicator=1, 16, 1024 data=<test multicast addrs> timeout=100 chain=1 size=<min pdu> data=<test multicast headers> | status=ok rx <indicator> frames: verify frame headers match expected headers (data) and frame contents are test pattern |
| active, delmulti | bind, enable, addmulti, delmulti, rx (rx to verify receive timeout on invalid multicast addrs) | indicator=1, 16, 1024 data=<test multicast addrs> timeout=5 chain=1 size=<min pdu> data=<test multicast headers> | status=ok timeout triggered |
| active, allmultion | bind, enable, allmultion, rx (rx to verify receive on multiple multicast addresses) | timeout=5 chain=1 size=<min pdu> data=<test multicast headers> | status=ok verify actual frame headers match expected headers (data) and frame contents are test pattern |
| active, allmultioff | bind, enable, allmultion, allmultioff, rx (rx to verify receive timeout on invalid multicast addrs) | status=ok indicator=0 timeout=5 chain=1 size=<min pdu> data=<test multicast headers> | status=ok timeout triggered |
| active, getcurrmac | bind, enable, getcurrmac |  | status=ok |
| active, setcurrmac | bind, enable, setcurrmac, rx (rx to verify receive on current unicast address) (getcurrmac verify addr) | data=<test_unimac_addr> | status=ok verify receive on test_unimac_addr data=<test_mac_addr> |
| active, getfactmac | bind, enable, getfactmac |  | status=ok data=<valid_mac_addr> |
| active, promiscon | bind, enable, promiscon, rx (rx to verify receive on test unicast address) |  | status=ok verify receive on test unicast mac address |
| active, promiscoff | bind, enable, promiscon, promiscoff, rx (rx to verify no receive on test unicast address) |  | status=ok verify receive timeout triggered |
| active, hwreset | bind, enable, hwreset |  | status=ok |
| active, badrxpkt | bind, enable, badrxpkt | indicator=0, repeat: indicator=<max_pdu> | status=ok |
| bound, info | bind, info | reset_statistics=false timeout=<tbd> repeat, reset_statistics=true | interface_is_active=true verify info returns zero’d stats |
| enabled, info | bind, enable, info | reset_statistics=false timeout=<tbd> adapter unplugged | interface_is_active=true |
| active, info | bind, enable, info | reset_statistics=false timeout=<tbd> | interface_is_active=true |
| unbound, info | info, bind | reset_statistics=false timeout=<tbd_long_time> | interface_is_active=true verify info_ack returned after bind_ack |
| enabled, status | bind, enable *unplug NIC*, status *plugin NIC*, status |  | event=down event=up |

## NIC Driver Invalid Operations Test Case

The NIC driver invalid operations test case verifies driver behavior when presented with state transitions that are not valid according to the UDI NIC Driver Specification. This test case also verifies driver behavior when operations with invalid parameters are attempted.

In the Functional Test column, state transitions are delineated with arrows (->) between two states. Operations attempted in a given state are marked <state>, <operation>.

The Test Purpose Sequences assume the driver has been initialized by the Management Agent and received a udi_channel_event_ind(UDI_CHANNEL_BOUND) on the NSR’s parent channel.

| Functional Test | Test Purpose Sequence | Input Parameters/Notes | Expected Results |
| --- | --- | --- | --- |
| unbound->transmit | tx | chain=1 size=<min to max pdu> data=<valid_header> urgent=false | rx machine verifies no frames sent on wire |
| unbound->receive | rx | timeout=<tbd> chain=1 size=<min to max pdu> data=<valid_header> | timeout triggered tx machine sends frames to broadcast address |
| bound->transmit | bind, tx | chain=1 size=<min to max pdu> data=<valid_header> urgent=false | rx machine verifies no frames sent on wire |
| bound->receive | bind, rx | timeout=<tbd> chain=1 size=<min to max pdu> data=<valid_header> | timeout triggered tx machine sends frames to broadcast address |
| enabled->transmit->bound | bind, enable, tx, disable | adapter unplugged | rx machine verifies no frames sent on wire |
| bound, bind | bind, bind |  | status=invalid_state |
| enabled, bind | bind, enable, bind | adapter unplugged | status=invalid_state |
| active, bind | bind, enable, bind | status=invalid_state | status=invalid_state |
| unbound, unbind | unbind |  | status=invalid_state |
| unbound, enable | enable |  | status=hardware_problem |
| enabled, enable | bind, enable, enable | adapter unplugged | status=hardware_problem |
| active, enable | bind, enable, enable |  | status=hardware_problem |
| active, tx | bind, enable, tx | chain=1 size=<max pdu + 1> data=<valid_header> urgent=false | rx machine verifies no frames sent on wire |
| active, tx | bind, enable, tx | chain=1 size=<min pdu - 1> data=<invalid_header> urgent=false | rx machine verifies no frames sent on wire |
| unbound, disable | disable |  |  |
| bound, disable | bind, disable |  |  |
| bound, ctrl | bind, getfactmac |  | status=not_understood |
| unbound, info | info | reset_stats=false timeout=<tbd> | timeout triggered |
| active->unbound, info | bind, enable, unbind, info | reset_stats=false timeout=<tbd> | timeout triggered |

## NIC Driver Stress Test Case

The NIC driver stress test case verifies driver behavior under heavy load.

This test case measures and reports %media saturation and %cpu utilization.

| Operation | Test Purpose Sequence | Input Parameters | Expected Result |
| --- | --- | --- | --- |
| transmit | bind, enable, tx (loop) | chain=<all_tx_cbs> size=<min to max pdu> data=<valid_header> urgent=false | receiver verifies frame headers matchs expected headers (data) and frame contents are test pattern and generates pass/fail |
| receive | bind, enable, rx (loop) | timeout=<tbd> chain=1 size=<min to max pdu> data=<valid_header> | rx_status=0 actual_frame_size=size actual_frame_header=data frame_data=<testpattern> (for all frames) |

## NIC Driver Multiple Adapter Test Case

The NIC driver multiple adapter test case verifies the driver is able to utilize more than one adapter for both send and receive. Unlike the stress test case, this test case does not attempt to put the driver under extreme load.

| Test | Test Purpose Sequence | Input Parameters/Notes | Expected Results |
| --- | --- | --- | --- |
| transmit | bind, enable, tx (on all supported adatpers) | chain=<1> size=<min to max pdu> data=<valid_header> urgent=false TBD - timed test? | receiver verifies frame header matches expected header (data) and frame contents are test pattern and generates pass/fail |
| receive | bind, enable, rx (on all supported adapters) | timeout=<tbd> chain=1 size=<min to max pdu> data=<valid_header> TBD - timed test? | rx_status=0 actual_frame_size=size actual_frame_header=data frame_data=<testpattern> |